DUO S TC R washbasin

Reference: 160360

CCTP description

Wall-mounted washbasin with through-the-wall installation for service ducts.

Integrated countertop.

Basin on the right.

Basin internal diameter: 310mm.

Bacteriostatic 304 stainless steel. Polished satin finish. Stainless steel thickness: 1.2mm

Rounded edges prevent injury.

Vandal-resistant: shrouded basin.

200mm threaded rod can be cut to size (other lengths are available on request).

Recessed horizontal waste outlet Ø 1".

Flat perforated waste, without screws:

easy cleaning and vandal-resistant.

Without overflow. Supplied with fixing elements.

CE marked. Complies with European standard EN 14688. Weight: 8.5kg.

[Formerly ref: 0216360000]