Mechanical  basin mixer H.  40mm L.  115mm

Reference: 2221L

CCTP description

Mechanical basin mixer H. 40mm L. 115mm with hygienic flow straightener.

Ø 40mm ceramic cartridge.

Pre-set maximum temperature limiter.

Flow rate limited to 5 lpm at 3 bar.

Hygiene control lever L. 150mm.

Without pop-up waste.

Supplied with PEX flexibles F3/8".

Reinforced fixing via 2 stainless steel rods.

10-year warranty.