Mechanical  basin mixer H. 85 L. 135

Reference: 2521

CCTP description

Mechanical basin mixer H. 85mm L. 135mm with BIOSAFE hygienic outlet.

Ø 40mm ceramic cartridge.

Pre-set maximum temperature limiter.

Flow rate limited to 5 lpm at 3 bar.

Sculptured control lever.

Without pop-up waste.

Supplied with PEX flexibles F3/8".

Reinforced fixing via 2 stainless steel rods.

10-year warranty.