2620MINI

BIOSAFE mechanical basin mixer

Reference: 2620MINI

Specification Description

Mechanical basin mixer H. 55mm L. 80mm with BIOSAFE hygienic outlet integrated into the body.

Securitouch thermal insulation prevents burns.

Ø 35mm ceramic cartridge.

Pre-set maximum temperature limiter.

Thermal shocks are possible without removing the control lever or shutting off the cold water supply.

Body with smooth interior and very low water volume (reduces bacterial development).

Flow rate limited to 4 lpm at 3 bar.

Solid control lever.

Chrome-plated stainless steel body.

Ergonomic pop-up waste 1 1/4" in brass.

Reinforced fixing via two stainless steel rods.

Stainless steel braided PEX flexibles F3/8", rotating unions.