26216EP

SECURITHERM EP BIOSAFE pressure-balancing basin mixer

Reference: 26216EP

Specification Description

SECURITHERM basin mixer H. 95mm L. 110mm with pressure balancing and BIOSAFE hygienic outlet integrated into the body.

Anti-scalding safety: HW flow rate is reduced if CW supply fails.

Securitouch thermal insulation prevents burns.

Ø 35mm ceramic cartridge with pressure balancing.

Pre-set maximum temperature limiter.

Thermal shocks are possible without removing the control lever or shutting off the cold water supply.

Body with smooth interior and very low water volume (reduces bacterial development).

Flow rate limited to 4 lpm at 3 bar.

Solid control lever.

Chrome-plated stainless steel body.

Mixer without pop-up waste.

Reinforced fixing via two stainless steel rods.

Supplied with copper tails and Ø 15mm stopcocks.