SECURITHERM EP basin mixer H. 85mm L. 120mm

Reference: 2721TEP

CCTP description

SECURITHERM pressure-balancing basin mixer with spout H. 85mm L. 120mm with hygienic flow straightener.

Anti-scalding safety: HW flow rate is reduced if cold water supply fails (and vice versa).

Ø 40mm ceramic cartridge with pressure-balancing.

Pre-set maximum temperature limiter.

Body and spout with smooth interiors and low water volume (reduced bacterial development).

Flow rate limited to 5 lpm at 3 bar.

Solid control lever.

Without pop-up waste.

Supplied with F3/8" PEX flexibles with filters and non-return valves.

Reinforced fixings via 2 stainless steel rods.

10-year warranty.