BINOPTIC MIX

Reference: 379MCH

CCTP description

Cross wall electronic basin mixer:

Independent IP65 electronic control unit.

230/12V mains supply with transformer.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 to 6 lpm.

Scale-resistant flow straightener.

Adjustable duty flush (pre-set flush ~60 seconds every 24 hours after last use).

Active, infrared presence detection, sensor at the end of the spout optimises detection.

Filters and solenoid valves M3/8".

Chrome-plated brass body.

Chrome-plated spout for cross wall installation ≤110mm

Cable for sensor L. 120mm, flexibles and mounting all pass through the same hole.

Anti-blocking safety.

Spout with smooth interior and low volume of water (reduces bacterial niches).

Side temperature control with standard lever and adjustable maximum temperature limiter.

10-year warranty.