TEMPOMATIC MIX 4

Reference: 490000

CCTP description

Deck-mounted electronic basin mixer:

230/6V recessed mains supply.

Reduced-stagnation solenoid valve and electronic unit integrated into the body of the mixer.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 - 6 lpm.

Scale-resistant flow straightener.

Duty flush (~60 seconds every 24 hours after last use).

Active, infrared presence detection, sensor at the end of the spout optimises detection.

Chrome-plated solid brass body.

Cap fixed in place by 2 concealed screws.

PEX flexibles, stopcocks F3/8", filters and non-return valves.

Fixing reinforced by 2 stainless steel rods.

Anti-blocking safety.

Side temperature control with adjustable maximum temperature limiter.

10-year warranty.