TEMPOFIX 3 frame system for urinals

Reference: 543006D-430006

CCTP description

Frame system W. 430mm for urinals:

Black powder-coated steel frame for wall-mounted installation.

Fixes to floor and load-bearing walls with anchoring bolts supplied.

Adjustable bracket 100 - 280mm.

Frame height can be adjusted from 0 - 200mm.

Ø 50mm soil pipe with waterproof seal.

Delivered pre-mounted.

Complies with French standard NF D12-208.

Compatible with wall finishes 13 - 120mm.

Fitted with TEMPOMATIC 4 F1/2" direct flush electronic valve:

Operated by 123 6V Lithium batteries.

Satin stainless steel plate 145 x 145mm with integrated electronics.

Shock-resistant infrared presence detection sensor.

Waterproof recessing housing.

Detection delay is 10 seconds.

3 programmes (rinsing volume can be adjusted according to urinal type).

High frequency mode (exclusive to DELABIE).

Hygienic duty flush every 24 hours (can be adjusted to 12 hours or OFF) after last use: prevents vacuums.

Flow rate pre-set at 0.15 L/sec at 3 bar, can be adjusted.

Connection with 1/2" brass connection (for urinal valves with flexible supply).

Technical features: see TEMPOMATIC urinal ref. 430PBOX-430006.

10-year warranty.