TEMPOFIX 3 self-standing frame system for WCs

Reference: 547005-546412

CCTP description

Self-supporting frame system W. 350mm for wall-hung electronic WC:

Black powder-coated steel frame.

Fixes to load-bearing floors.

Frame height can be adjusted from 0 - 200mm (with 1m mark).

Ø 32mm flush tube with Ø 55mm connection washer.

PVC soil pipe, Ø 100mm outlet to be glued to waterproof seal, with 2 setting positions.

Delivered pre-mounted.

Complies with French standard NF D12-208.

Compatible with solid walls from 26 - 130mm.

Fitted with TEMPOMATIC F1" electronic direct flush valve:

Mains supply with 1" solenoid valve.

Stainless steel wall plate 320 x 220mm.

IP65 independent electronic unit.

230/12V transformer.

Shock-resistant infrared presence detection sensor.

Voluntary activation flush when hand is detected ~10cm in front of the sensor or automatically when the user leaves.

Time flow ~7 seconds can be adjusted 3 - 12 seconds.

Integrated stopcock and flow rate and flush volume adjuster.

Detection distance can be adjusted by the installer.

Technical characteristics: see TEMPOMATIC WC ref. 463326.

10-year warranty.