TEMPOFIX 3 wall-mounted frame system for WCs

Reference: 564000-464000

CCTP description

Frame system W.350mm for wall-hung WCs:

Black powder-coated steel frame.

Wall-mounted frame system for fixing to load-bearing walls.

Frame height can be adjusted from 0 - 200mm (with 1m mark).

Ø 32mm flush tube with Ø 55mm connection washer.

PVC soil pipe, Ø 100mm outlet to be glued to waterproof seal, with 2 setting positions.

Delivered pre-mounted.

Complies with French standard NF D12-208.

Compatible with solid walls from 10 - 120mm.

Fitted with TEMPOMATIC dual control F¾" electronic direct flush valve:

230/6V mains supply (cable and transformer supplied).

Satin finish stainless steel wall plate 186 x 186mm and chrome-plated metal button with integrated electronics.

Waterproof recessing housing.

Detection delay is 10 seconds.

Voluntary activation (push-button with anti-blocking) or automatically when the user leaves.

"Intelligent" automatic rinsing (flush volume adapts according to use).

3 programmes (rinsing volume can be set according to type of WC pan).

Hygienic duty flush, every 24 hours (can be adjusted to 12 hours or OFF) after the last use.

Technical characteristics: see TEMPOMATIC dual control ref. 464SBOX-464000.

10-year warranty.

Provisional availability 2nd half 2019, please contact the sales office to check availability.