TEMPOFIX 3 with TEMPOFLUX 3 AB

Reference: 564065-763000

CCTP description

Self-supporting frame system W. 350mm for wall-hung WC pans:

- Black powder-coated steel frame.

- Fixes to load-bearing floors.

- Frame height can be adjusted from 0 - 200mm (with 1m mark).

- Ø 32mm flush tube with Ø 55mm connection washer.

- Ø 100mm PVC soil pipe and PVC collar with waterproof seal, with 2 setting positions.

- Delivered pre-mounted.

- Complies with French standard NF D12-208.

- Compatible with solid walls from 10 - 120 mm.

Fitted with a TEMPOFLUX 3 F3/4'' time flow direct flush valve:

- Satin finish stainless steel wall plate 210 x 162mm.

- Waterproof recessing housing.

- Soft-touch operation.

- Dual flush 3L/6L, can be adjusted to 2L/4L.

- AB anti-blocking system.

- Backflow prevention device inside the housing.

- Integrated stopcock and flow rate adjuster.

- Acoustic level complies with NF EN 12541 class II.

- Compatible with sea water and grey water.

For technical features see TEMPOFLUX 3 ref. 763BOX-763000.

10-year warranty.

Available 2nd half 2019, please contact the sales office to check availability.