6607D

Wall-mounted paper towel dispenser, for 750 sheets

Reference: 6607D

Specification Description

Wall-mounted paper towel dispenser.

With lock and standard DELABIE key.

With level control.

Capacity 750 sheets.

Stainless steel thickness: 1mm.

Polished satin stainless steel.

Dimensions: 130 x 275 x 450mm.

Pack of 250 folded paper towels can be ordered separately (ref. 6606).

Paper towel dimensions: open 230 x 250 mm, closed 115 x 250 mm.