TEMPOFLUX 3 recessed WC AB

Reference: 763BOX-763040

CCTP description

TEMPOFLUX 3 waterproof, recessed time flow direct flush valve:

Chrome-plated metal wall plate 170 x 170mm.

Waterproof recessing housing:

- Collar with waterproof seal.

- Hydraulic connection to the outside and maintenance from the front.

- Adjusts to all types of installation (rails, solid walls, panels).

- Compatible with wall finishes from 10 - 120mm (while maintaining the minimum recessing depth of 93mm).

- Suitable for standard or "pipe-in-pipe" supply.

- Stopcock and flow rate adjustment, activation unit and cartridge are all integrated and accessible from the front.

- TEMPOFLUX 3 F3/4" flush valve is compatible with sea water and grey water.

- Back flow prevention device inside the housing.

- Supplied in 2 kits: secure system flush without sensitive elements.

Soft-touch operation.

AB Anti-blocking system: flush only takes place once the push-button is released.

Dual flush 3L/6L can be adjusted to 2L/4L.

Outlet connection for PVC tube Ø 26/32mm.

Acoustic level complies with European standard EN 12541 (class II acoustic level).

Suitable for Rimless WC pans.

10-year warranty.

Provisional availability 2nd half of 2019, please contact sales office for more details.