SECURITHERM shower panel

Reference: 792330

CCTP description

Securitherm dual control thermostatic time flow shower panel:

Anodised aluminium shower panel for wall-mounted, exposed installation.

With concealed inlet via flexibles, M½".

SECURITHERM thermostatic mixer.

Adjustable temperature control from cold water up to 38°C

with 1st limiter set at 38°C and 2nd limiter set at 41°C.

Anti-scalding safety: automatic shut-off if cold water supply fails.

Thermal shocks are possible.

Time flow valve ~30 seconds with soft-touch operation.

Chrome-plated, tamperproof, scale-resistant ROUND shower head with automatic flow rate regulation at 6 lpm at 3 bar.

Handset with removable flexible via push-fit rapid STOP connector and wall support supplied.

Concealed fixings.

Filters and non-return valves.

10-year warranty.