SECURITHERM shower panel

Reference: 792340

CCTP description

Dual control thermostatic shower panel:

Anodised aluminium shower panel for wall-mounted, exposed installation.

Top inlets via in-line stopcocks, M1/2".

SECURITHERM thermostatic mixer.

Adjustable temperature control from cold water up to 38°C; with 1st limiter set at 38°C and 2nd limiter set at 41°C.

Anti-scalding safety: automatic shut-off if cold or hot water supply fails.

Time flow valve ~30 seconds with soft-touch operation to control the ROUND shower head.

Non-time flow valve controls the hand set.

Thermal shocks are possible.

Chrome-plated, tamperproof, scale-resistant ROUND shower head with automatic flow rate regulation at 6 lpm at 3 bar.

Handset with removable flexible via rapid push-fit STOP connector and wall support supplied.

Concealed fixings.

Filters and non-return valves.

10-year warranty.