SECURITHERM Shower Panel

Reference: 792410

CCTP description

Electronic thermostatic shower panel:

Anodised aluminium shower panel for wall-mounted, exposed installation.

SECURITHERM thermostatic mixer.

With concealed inlet via flexibles, M1/2".

Adjustable temperature control from cold water up to 38°C with 1st limiter set at 38°C and 2nd limiter set at 41°C.

Anti-scalding safety: instant shut-off if cold water supply fails.

Thermal shocks are possible.

Battery-operated with 223 6V Lithium battery.

Infrared presence detection. Shower starts when hand is 4cm from the sensor.

Shuts off on demand or automatically after ~60 sec.

Duty flush (~60 seconds every 24 hours after the last use).

Flow rate set at 6 lpm at 3 bar.

Chrome-plated, tamperproof, scale-resistant ROUND shower head with automatic flow rate regulation.

Concealed fixings.

Filters and non-return valves.

10-year warranty.